## Slide 1
SkillUp Hackathon in collaboration with IBM SkillsBuild
NATIONAL FINALE
Solar Hybrid Agri Cool Hub : Solar-Powered Smart Crop Preservation and Transportation Monitoring System
COLLEGE NAME
G. Pulla Reddy Engineering College
TEAM NAME
Limited Edition
TEAM MEMBERS
N. HARSHAVARDHAN, M. BHARANI KUMAR REDDY, T. SHIREESHA, S. SAI SHARATH, S. NASEEHA MASHRATH

## Slide 2
Problem & Solution Statement
Problem Statement
Solution Statement
Who is Affected
Small holder farmers & transport operators in rural India face significant post-harvest crop losses due to unmonitored storage conditions during transportation.
Key Challenges
No way to monitor temperature, humidity, or gas levels inside a sealed moving storage unit.
Spoilage is discovered only at the destination too late to save the produce.
Limitations of Existing Solutions
Commercial cold-chain IoT systems are priced for large logistics companies unaffordable for small farms.
Manual checks are infrequent, unreliable, and provide no real-time data.
No affordable, solar-capable, connected solution exists for last-mile agricultural transport.
Proposed solution Solar Hybrid Agri Cool Hub: an IoT-powered smart preservation system that actively cools (Peltier module), humidifies (solar-powered), and continuously monitors crop storage conditions.
How It Works
Sensors measure temp, humidity & gas every 15 s → encrypted to cloud → alert engine → farmer notified instantly on Android app or web dashboard.
Key Features & Benefits
Real-time alerts (WARNING & CRITICAL) before spoilage occurs time to act.
Offline resilience no data lost during connectivity outages; replayed automatically.
Solar-hybrid power reduces electricity costs for rural, off-grid deployments.
Impact
Reduced post-harvest losses → higher crop quality → better farmer income → sustainable food supply chains.

## Slide 3
Project Architecture & IBM Bob Technology
Project Architecture:
SYSTEM COMPONENTS
ESP32-S3 - C/C++ - SHT4x - MQ-3 / MQ-135 / MQ-4 - INA219 - GPS - RTC
Hardware & Firmware
Communication
HiveMQ Cloud MQTT QoS 1, TLS, Last Will and Testament (LWT)
Backend API
Python 3.11 - FastAPI - Pydantic validation - Alert engine - SSE
Database
PostgreSQL 15 - Stores devices, telemetry, alerts, and thresholds.
Client Applications
Android (Java/Kotlin) - React dashboard –
Retrofit - Recharts
Sensors Collect Data
Create Telemetry
MQTT Transmission
Backend Processing
Database Storage
User Applications
/devices • /status • /telemetry • /alerts/active • /thresholds • /stream • /health
IBM Bob - Role in Development : PLAN  AGENT ASK
Planning: PLAN
Helped design end-to-end IoT architecture.
Defined JSON schema, MQTT topics, database models, and alert logic.
Planned API structure and client applications.
Code Generation: AGENT
Assists with modular ESP32 firmware (sensor reading, MQTT, JSON serialization).
Generates FastAPI backend (APIs, MQTT subscriber, alert engine).
Develops Android app (Java/Kotlin UI, charts, maps).
Debugging: ASK+AGENT
Helps investigate MQTT payload issues.
Resolves sensor scaling and ADC problems.
Fixes API schema mismatches and database errors.
Troubleshoots network, TLS, and connection failures.
Supports integration of hardware, backend, and mobile app.




