## Slide 1
Project Architecture | IBM Bob Technology
PROJECT ARCHITECTURE — Components, Technologies & Data Flow
1 HARDWARE
ESP32-S3 N16R8
Arduino / ESP-IDF C++
SHT4x Temp+RH
MQ-3 Ethanol Gas
MQ-135 Air Quality
MQ-4 Methane
INA219 Solar Power
NEO-6M GPS
DS3231 RTC
PSRAM 60-msg Buffer
MQTT TLS
Port 8883
QoS 1
2 MQTT BROKER
HiveMQ Cloud
Port 8883 TLS
MQTT v3.1.1
QoS Level 1
LWT ONLINE/OFFLINE
TLS Encrypted
Auto-reconnect
aiomqtt
Python
asyncio
3 BACKEND API
FastAPI Python 3.11
Uvicorn + asyncio
Pydantic v2 Validation
MQTT Ingestion
Alert Engine
SSE Live Stream
REST 9 Endpoints
Idempotent Migrations
asyncpg
SQLAlchemy
2.x async
4 DATABASE
PostgreSQL 15
SQLAlchemy async
devices table
telemetry table
alerts table
thresholds table
(device_id,timestamp)
unique constraint
REST API
+ SSE
Stream
5 CLIENT APPS
Android Java/Kotlin
React 19 TypeScript
Retrofit 2 + OkHttp
MPAndroidChart 24h
Recharts Line Charts
SSE Live Cards
Lottie Splash
SharedPreferences
DATA FLOW:
Sensors Read (1s) → JSON Built (10 fields) → MQTT TLS Publish (15s) → Validated + Stored → Alert Evaluated (WARNING/CRITICAL) → SSE Pushed → Farmer Notified
KEY APIs: GET /devices | GET /devices/{id}/status | GET /devices/{id}/telemetry | GET /alerts/active | PATCH /alerts/{id}/resolve | PUT /devices/{id}/thresholds | SSE /devices/{id}/stream | GET /health
IBM BOB TECHNOLOGY — Role in the Development Process
PLANNING & ARCHITECTURE
• Designed full 5-layer system before any code
• Defined exact JSON payload all layers agreed on
• Specified all MQTT topics, DB schema, API contracts
• Designed WARNING/CRITICAL alert model
• Planned (device_id, timestamp) dedup strategy
CODE GENERATION
• All 18 C++ firmware modules (sensors, Wi-Fi, MQTT)
• Entire FastAPI backend — routes, MQTT, SSE, alerts
• React useSyncExternalStore SSE hook for live cards
• Retrofit interface + Android fragments (Java)
• SVG radial gauge with threshold colour transitions
DEBUGGING
• Silent data loss: str(bytes) → .decode() in MQTT
• Hardware damage prevented: voltage divider for MQ ADC
• Android NullPointerException: ViewBinding lifecycle fix
• SSE DB pool exhaustion: close session before sleep
• GPS freeze: non-blocking byte-by-byte UART drain
TESTING & DOCUMENTATION
• 24 pytest tests on in-memory SQLite (no real DB)
• Tests: schema validation, alerts, dedup, all endpoints
• 8 documentation files: wiring, API, deploy, config
• Idempotent startup schema migrations (zero data loss)
• 48-decision engineering log (DECISIONS.md)
IBM Bob Impact: 4 Tech Stacks Covered | 18 Firmware Modules Generated | 24 Automated Tests Written | 8 Documentation Files Authored | 5 Critical Bugs Fixed
Notes: Slide covers two required sections: Project Architecture (5-layer flow: Hardware → MQTT → FastAPI → PostgreSQL → Android/React, with data flow and 8 APIs) and IBM Bob Technology (Planning, Code Generation, Debugging, Testing & Documentation).